## Slide 1: Emergency Navigation Homework Solutions
Global Navigation
Chapter 7

## Slide 2: Learning Objectives
Provision an emergency navigation kit.
Construct emergency plotting charts
Determine destination coordinates mathematically from course and distance traveled.

## Slide 3: Question 1
A vessel travels 52nm on course 060°T from L31°35’N, Lo 19°40’W. Find the coordinates of the point of arrival.
Answer : L32°01’N, Lo018°41’W

## Slide 4: Question 2
On 16 July, a sailboat crew on a course of 070°T, position L25°00´N, Lo 30°00´W, experiences a fire and is forced to escape on their motorless dinghy. After three days of drifting with the current, what is their approximate position? (Hint: Use Pilot Chart NO 16 from your Junior Navigation course material for current information.)
Answer: L 24°38´N, Lo 30°32´W
Solution: From the pilot chart, you determine that the probable current in that area is 0.5kn at 230°. Therefore, the distance traveled =
0.5kn x 3days x 24hr/day = 36 nm.
See completed Simplified Traverse Worksheet,

## Slide 5: Question 3
On 22 June, the fishing vessel, Myra D, left Kaena Point, Hawaii for a week’s fishing trip. At ZT 2100, the vessel left its position of L21°49’N, Lo158°53’W on a course of 215°T and a speed of 9kn. Current was deemed negligible. On 23 June at ZT 1900, an engine room fire quickly spread and forced the captain and three crew members to abandon the vessel and board the boat’s two life rafts, which they tied together.

## Slide 6: Question 3a
Using the Simplified Traverse Table, calculate the approximate position at the time of vessel abandonment.
Answer L19°11’N, Lo161°05’W
Solution: Calculate the distance traveled from the time of departure to the time of vessel abandonment.
ZT 2100 22 june
ZT 1900 23 june
22 hours travel
Distance traveled = 9 kn X 22 hrs = 198 nm.

## Slide 7: Question 3b
At approximately ZT 1949, one of the crew identified the star Arcturus directly overhead. What was their approximate position at that time?
Answer : L19°10’N, Lo161°03’W.
Solution:
Since Arcturus is directly overhead, we are at the GP of the body.
To find our latitude and longitude, convert Arcturus’s celestial coordinates for that date and time to terrestrial coordinates.
Solution:
ZT 1949 23 june
ZD +11
UT 3049 23 june
-24 hres + 1 day
UT 0649 24 june
Solution:
From the Nautical Almanac for the date 24 Jun, 20XX, we find that the SHA of Arcturus = 146°01.9’, and the declination of Arcturus = 19°09,7’N.
Since observer’s latitude = the declination of the body overhead, latitude is approximately L 19°10’N.
Solution:
To calculate longitude, we calculate the GHA of Arcturus at the time of the sighting :
GHA (Arcturus) = GHA (Aries) + SHA (Arcturus)
Solution:
24 june
GHA Aries 0600 hours 2°43,8’
49 minutes 12°17,0’
GHA Aries 0649 15°00,8’
SHA Arcturus 146°01,9’
GHA Arcturus 161°02,7’
Since GHA<180°, GHA = LoW, so our approximate longitude is: Lo161°03’W.

## Slide 8: Emergency Navigation
End of
Global Navigation
Chapter 7