## Slide 1: Taking Sights and Finding Ho, LHA and Dec
Global Navigation
Homework Solutions
Chapter 3

## Slide 2: Objectives
Demonstrate and describe techniques for taking sights on moon, planets & stars.
Apply proper altitude corrections for these sights to deterimine Ho.
Apply proper corrections for low altitude sights on any celestial body.
Understand & apply new concepts of celestial coordinates.
Compute LHA and Dec for each sextant observation.

## Slide 3: Question 1
In the daily pages, the «v» value for the planets:
a) is always positive.
b) is positive except for Venus, which can be either positive or negative.
c) depends on the declination of the body.
d) is applied East or West to GHA.
Ref: ¶ 83

## Slide 4: Question 2
In the daily pages, the «d» value for the planets is:
a) always positive.
b) positive except for Venus, which is negative.
c) positive or negative depending on the trend of the declination tabulated in the daily pages.
d) positive or negative depending on whether declination is North or South.
Ref.: ¶ 84

## Slide 5: Question 3
The value of d tabulated in the daily pages is:
a) the declination increment and always positive.
b) the average amount by which the declination of a body changes in one hour.
c) the variable rate of change in GHA during one hour.
d) not applied to the sun or moon.
Ref.: ¶ 84

## Slide 6: Question 4
The declination of a body at 1423 UT is 20°16’N, and at 1523 UT is 20°29,4’N. The d value for this body is:
a) between 0,0’ and 0,1’.
b) between 0,1’ and 1,0’.
c) between 1,0’ and 5,0’.
d) greater than 5,0’.
Ref.: ¶ 84

## Slide 7: Question 5
The body in the previous question is probably:
a) the sun.
b) the moon.
c) Saturn.
d) Achernar.
Ref.: ¶ 84

## Slide 8: Question 6
The v correction is:
a) found in the daily pages.
b) the amount by which the hourly change in GHA differs from the average rate of change for the body.
c) the amount by which declination changes in one hour.
d) the amount by which GHA changes in one hour.
Ref.: ¶ 82

## Slide 9: Question 7
Which of the following magnitudes is the brightest?
a) 2,3
b) 1,5
c) -1,7
d) -2,0
Ref.: ¶ 73

## Slide 10: Question 8
Which of the following could be a reasonable value of GHA increment for any celestial body in approximately one-half hour?
a) 3°26,7’
b) 7°25,2’
c) 14°54,2’
d) 29°58,7’
Ref.: ¶ 81

## Slide 11: Question 9
The sign of the v correction for the moon:
a) is always positive.
b) is always negative.
c) can be positive or negative depending on the direction of change in successive hourly values.
d) is positive when the declination of the moon is North.
Ref.: ¶ 83

## Slide 12: Question 10
For the following problems, use the Excerpts from the Nautical Almanac, Appendix B and the Increments and Corrections tables from any Almanac. Find GHA, LHA and the declination of each of these bodies.
Moon UL;06-20-09 UT; 28 March; Lo 070°14,7’W
Moon LL; 13-17-14 UT; 30 March; Lo 165°51,1’E
Mars; 14-04-23 UT; 28 March; Lo 009°21,8’W
Venus; 07-27-27; 30 March; Lo 130°36,1’E
Schedar; 02-27-09; 23 August; Lo 079°41,5’E
Rigel; 23-11-34; 24 August; Lo 074°59,2’W
Moon UL; 06-20-09 UT; 28 March; Lo 070°14,7’W
GHA 06- 00 186°12,5’ Dec 27°19,6’N
20- 09 +4°48,5’ d (+)1,8
v 10,1 corr. v +3,5’ corr. d + 0,6’
Total GHA 191°04,5’ Total D. 27°20,2’N
Lo -070°14,7’W
LHA 120°49,8’
Moon LL;13-17-14 UT;30 March;Lo 165°51,1’E
GHA 13- 00 262°43,1’ Dec 25°38,4’N
17-14 +4°06,7’ d (-)5,6
v 10,1 corr. v +2,9’ corr. d -1,6’
Total GHA 266°52,7’ Total Dec 25°36,8’N
Lo +165°51,1’E
432°43,6’
-360°
LHA 72°43,8’
Mars; 14-04-23 UT; 28 March; Lo 009°21,8’W
GHA 14-00 333°51,1’ Dec 22°10,4’N
04-23 +1°05,8’ d (+)0,3
v 0,8 corr. v +0,1’ corr. d + 0,0’
Total GHA 334°57,0’ Total Dec 22°10,4’N
Lo -009°21,8’W
LHA 325°35,2’
Venus; 07-27-27; 30 March; Lo 130°36,1’E
GHA 07-00 240°19,6’ Dec 22°20,6’N
27-27 +6°51,8’ d (+)0,8
v -0,0 corr. v -0,0’ corr. d + 0,4’
Total GHA 247°11,4’ Total Dec 22°21,0’N
Lo +130°36,1’E
377°47,5’
-360°
LHA 17°47,5’
Schedar; 02-27-09; 23 August; Lo 079°41,5’E
SHA 349°48,3’ Dec 56°33,6’N
GHA♈ 02-00 1°42,3’
27-09 +6°48,4’
Total GHA 358°19,0’ Total Dec 56°33,6’N
Lo +079°41,5’E
438°00,5’
-360°
LHA 78°00,5’
Rigel; 23-11-34; 24 August; Lo 074°59,2’W
SHA 281°18,8’ Dec 8°11,5’S
GHA♈ 23-00 318°33,2’
11-34 +2°54,0’
602°46,0’
-360°
Total GHA 242°46,0’ Total Dec 8°11,5’S
Lo -074°59,2’W
LHA 167°46,8’

## Slide 13: Question 11
On 1 March your DR position is L29°07.4'N, Lo 034°15,8'W. At 18-31-04 you obtain a sight on Sirius with an Hs of 36° 56,5'. A few minutes later at 18-36-15 you take a sight on Mars with an Hs of 60°32,0'. Both sights are taken on a natural horizon. Watch error is 00-0 sec; index correction is 0,0', height of eye 15 ft. Complete the sections of a USPS SR96 form needed to determine LHA, Dec, and Ho, and complete the Time Diagrams for each sight. Use Appendix B, “Excerpts from the Nautical Almanac” and the “Increments and Corrections” tables from any Almanac.
Body LHA Dec Ho
11a. Sirius 332°08,9' 16°43,4'S 36°51,4‘
11b. Mars 029°59,9' 17°58,7'N 60°27,7'

## Slide 14: Question 12
Find the average WT and Hs of the following data using one of the two methods described in this chapter.
Sight | WT |  | WT (decimals) | Hs | Hs (decimals)
10 | 18-56-02 |  | 18,93389 | 40⁰18,1’ | 40,30167⁰
11 | 18-57-10 |  | 18,95278 | 40⁰17,2’ | 40,28667⁰
12 | 18-58-18 |  | 18,97167 | 40⁰15,8’ | 40,26333⁰
13 | 18-59-43 |  | 18,99528 | 40⁰14,6’ | 40,24333⁰
14 | 19-01-01 |  | 19,01694 | 40⁰13,8’ | 40,23⁰
Sum |  |  | 94,87056 |  | 201,325⁰
Average |  | 18-58-27 | 18,97411 | 40⁰15,9’ | 40,265⁰
Columnar solution:
Sight No. WT Hs
10 18 -56 -02 40° 18.1’
11 18 -57 -10 40° 17.2’
12 18 -58 -18 40° 15.8’
13 18 -59 -43 40° 14.6’
14 19 18 -01 61 -01 40° 13.8’
Sum: 90 291 74
Avg: 18 290/5 134/5
Avg: 18 58 27

## Slide 15
Compute the latitude by the Polaris Tables method described in this chapter (and in the Nautical Almanac)?
Date 16 September
WT 18-03-52
WE 0-27 feet
HE 56 feet
Hs 42⁰ 49,1
IC -1,2
DR L 43⁰ 06,6’ N
DR Lo 069⁰ 22,8’ W
Question 13

## Slide 16: Taking Sights and Finding Ho, LHA and Dec
End of
Chapter 3