## Slide 1: Sunrise … Sunset
Global Navigation
Homework Solutions
Chapter 2

## Slide 2: Objectives
Understand the difference between local mean time and zone time and how to convert from one to the other.
Determine the ZT of sunrise, sunset, moonrise and civil and nautical twilight from the Nautical Almanac

## Slide 3: Question 1
The earliest time you can begin sextant observations in the morning is usually:
Shortly after the beginning of nautical twiliglight.
Shortly after the end od nautical twilight.
Shortly after the beginning of civil twilight.
Shortly after the end of civil twilight.
Ref: ¶ 14

## Slide 4: Question 2
The midpoint of the optimum observing time in the evening is usually around:
The beginning of nautical twilight.
The end of nautical twilight.
The beginning of civil twilight.
The end of civil twilight.
Ref: ¶ 14

## Slide 5: Question 3
If you are west of a zone meridian in east longitude, to convert LMT to ZT you would:
Add ZD
Subtract ZD
Add Dlo W (converted to time)
Subtract DLo E (converted to time)
Ref: ¶ 25

## Slide 6: Question 4
Determine the ZT of sunset and the end of evening civil twilight for the following dates and positions:
20 March L34⁰26,8’S Lo047⁰12,6’W
30 June L29⁰14,0’N Lo158⁰47,9’W
Solution 4 a
LMT SS LMT CT
L30⁰S 1811 1835
L35⁰S 1811 1836
Diff 5⁰ 0 +1
L34⁰26,8’S – L30⁰S = 4⁰26,8’ = 4.45⁰
Corr: 0 (4,45 ÷5) X 1 = 0,9 rounded to 1 min
L30⁰S 1811 1835
Corr. 0 + 1
L34⁰26,8’S 1811 1836
Solution 4 a (continued)
ZD +3, ZM Lo045⁰, DLo 2⁰12,6’ X 4 = 8 min 50,4 sec, rounded to 9 min
LMT SS LMT CT
LMT 1811 1836
Dlo (W) + 9 + 9
ZT 1820 1845

## Slide 7: Question 4 b - solution
LMT SS LMT CT
L30⁰N 1905 1933
L20⁰N 1843 1908
Diff 10⁰ +22 +25
L29⁰14,0’N – L20⁰N = 9⁰14,0’ = 9,23⁰
Corr: (9,23 ÷ 10) X 22 = 20 min.
(9,23 ÷ 10) X 25 = 23 min.
L20⁰ 1843 1908
Corr. + 20 +23
L29⁰14,0’ 1903 1931
ZD -11, ZM 165⁰ W, DLo 6⁰12,1’E X 4 = 24 min 48,4 sec., rounded to 25 min.
LMT SS LMT CT
LMT 1903 1931
DLo (E) -25 -25
ZT 1838 1906

## Slide 8: Question 5
Determine the ZT of moonrise et moonset for the following dates and positions :
A) 19 April L18°15,1’N Lo139°06,5’E
B) 24 Dec L51°32,2’S, Lo006°12,8’w
a) LMT Moorise LMT Moonset
L20°N 0535 1826
L10°N 0542 1817
Diff 10° -07 min + 9 m
L18°15,1’N – L10°N = 8°15,1’ = 8,255°
Corr: (8,25 ÷10) x 7 = 5,7, or 6, min
(8,25 ÷10) X 9 = 7,4, or 7,min
a) LMT Moonrise LMT Moonset
L10°N 0542 1817
Corr - 06 m + 07 m
L18°15,1’N 0536 1824
ZD +9, ZM Lo135°W, DLo 4°06,5’E X 4 =
16 min, 26 sec, rounded to 16 minutes.
LMT 0536 1824
DLo (E) -16 - 16
ZT 0520 1808
b) LMT Moonrise LMT Moonset
L50°S 1852 0149
L52°S 1905 0138
Diff 2° + 13 -11
L51°32,2’S – L50°S = 1°32,2’ = 1,54°
Corr (1,54 ÷2) X 13 = 10 min (1,54 ÷ 2) X 11 = 8,47, or 8 minutes
b) LMT Moonrise LMT Moonset
L50°S 1852 0149
Corr +10 - 08
L51°32,2’S 1902 0141
ZD +0, ZM 0⁰, DLo 6°12,8’W X 4 =
24 min, 51 sec, rounded to 25 minutes.
LMT 1902 0141
DLo (W) + 25 + 25
ZT 1927 0206

## Slide 9: Question 6
On 17 August, the 1500 GPS position of a vessel is L39°10’N, Lo144°06’E. Course is 110°T, and speed is 9,5 knots. The current is negligible. Determine the ZT of evening CT.
From the Almanac, the LMT of CT for L40°N on that date is 1922. Using this as CT, extend the intended track and measure the coordinates of the projected position for 1922. The plot places the DR of the 1922 position at L38°55,8’N, Lo144°56,0’E.
  L40°N 1922
L35°N 1912
Diff 5° + 10 m
L38°55,8’N – L35°N = 3°55,8’ = 3,93°
Corr (3,93 ÷5) X 10 = 7,86, or 8, min
L35°N 1912
Corr L38°55,8’ + 8 m
L38°55,8’N 1920
ZD -10, ZM 150°E, DLo 5°04,0’E X 4 =
20min 16 sec, rounded to 20 minutes
LMT 1920
DLo (W) +20
ZT 1940

## Slide 10: Sunrise … Sunset
End of
Chapter 2