## Slide 1: Sunrise … Sunset Quiz
Global Navigation
Chapter 2

## Slide 2: Question 1
If LMT is 1320, what is the ZT at 068°15’E?
Solution
68°15’ ÷15 = 4,55, ZD -5, ZM = Lo 075°E
DLo = 075° - 68°15’ = 6,75°
as DLo is west of ZM
(6,75° X 4 m/degree) = 27 minutes
LMT 1320
DLo (W) + 27
ZT 1347

## Slide 3: Question 2
If LMT is 0645, what is ZT at 152°40’W?
Solution
152°40’ ÷15 = 10,17, ZD + 10, ZM = Lo 150°
DLo = 152°40’ – 150° = 2°40’, as DLo is west of ZM
(2°40’ X 4m/degree) = 10,67, or 11, minutes
LMT 0645
DLo (W) + 11
ZT 0656

## Slide 4: Question 3
Your GPS position is L40°N, Lo035°15’W on 1 July. What is the ZT of morning NT?
Solution: From the Almanac daily pages, on 1 July, the morning NT for L40° is at 0320.
35°15’ ÷ 15 = 2,35; thus ZD + 2, ZM = 30°
DLo = 35° 15’ – 30° = 5° 15’
and DLo is west of ZM
(5°15’ X 4 m/degree) = 21 minutes
LMT 0320
DLo (W) +21
ZT 0341

## Slide 5: Question 4
On 10 May at ZT 0100, your GPS position is L35°50’N, Lo029°40’W. Course is 310°T, and speed is 8,5 knots. Find the ZT of morning CT?
Solution: From the Almanac, CT on 10 May will be at 0433 for L35°N. Based on your projection (see next table), your DR at that time will be L36°09,4’N, Lo030°08,6’W.
Solution part 2
Departure 0100 L35°50’N, Lo 029°40’W
Destination 0433 duration 213 minutes
60D = St, D = (8,5 X 213) ÷ 60 = 30,2 M
Angle C = 360°-310 = N50°W
ℓ = D X Cos C = 19,4’ or 0,323°
L2 = L1 + ℓ = 36°09,4’N, et Lm = 35,99°
P = D sin C = 23,1 milles westerly direction
DLo = 23,1 ÷ cos Lm = 28,6’
Lo2 = 29°40’O + 28,6’W = 030°08,6’W
Solution part 3
L 35°N 0433
L 40°N 0419
Diff 5° - 14 minutes
L36°09,4’N – L35°N = 1°09,4’ = 1,1567°
Corr (1,1567° ÷ 5) X 14 =
3,2386 rounded to 3 minutes
Solution part 4
L35°N 0433
Corr L36°09,4’ - 3
L36°09,4’N 0430
Lo 030°08,6 ÷ 15 = 2, ZD + 2, and ZM=30°
DLo = 30°08,6’ – 30° = 0°08,6’W
DLo 0°08,6’ W X 4 m/degree = 0,57, or 1, min
LMT 0430
DLO (W) +1
ZT 0431

## Slide 6: Question 5
In the morning, Nautical Twilight begins when the center of the sun is __________ below the celestial horizon and ends at ____________________.
12 degrees
at the beginning of CT

## Slide 7: Question 6
In the evening, Civil Twilight begins at _________________ and ends when the center of the sun is ________ below the celestial horizon.
sunset
6°

## Slide 8: Question 7
On 6 Dec, at ZT 1400 your GPS position is L30°05,0’N, Lo062°30,0’O. Your course is 315°T with a speed of 12 knots. What will be the ZT at the end of evening Civil Twilight?
Solution part 1
From the Almanac, the end of Civil Twiliglight on 6 Dec, for L30°N, is 1726. Based on your projection, your 1726 DR will be L30°34,1’N, Lo063°03,8’W.
Solution part 2
Departure 1400 L30°05’N, Lo 062°30’W
Destination 1726 duration 213 minutes
60D = St, D = (12 X 206) ÷ 60 = 41,2 M
Angle C = 360°-315 = N45°W
ℓ = D X Cos C = 29,1’ or 0,486°
L2 = L1 + ℓ = 30°34,1’N, and Lm = 30,33°
P = D sin C = 29,1 milles westerly direction
DLo = 29,1 ÷ cos Lm = 33,8’
Lo2 = 62°30’W + 33,8’W = 063°03,8’W
Solution part 3
L 30°N 1726
L 35°N 1716
Diff 5° - 10 minutes
L30°34,1’N – L30°N = 0°34,1’ = 0,568°
Corr (0,568° ÷ 5) X 10 = 1, 136
rounded to 1 minutes
Solution part 4
L30°N 1726
Corr L30°34,1’ - 1 L30°34,1’N 1725
Lo 063°03,8W ÷ 15 = 4,2, ZD + 4,
and ZM =060°, DLo = 63°03,8’ – 60° = 3°03,8’’W
DLo 3°3,8’ W X 4 m/degree = 12,25, or 12 m
LMT 1725
DLO (W) 12
ZT 1737

## Slide 9: Question 8
To find the exact time of moonrise, you must consider the effect of your longitude.
a) True
b) False

## Slide 10: Sunrise … Sunset Quiz
End
Global Navigation
Chapter 2